## Slide 1
ARDUINO
BESTIN AUTOMATION

## Slide 2: What is an Arduino ?
Open Source electronic prototyping platform based on flexible easy to use hardware and software.

## Slide 3: Arduino
Arduino is an open-source electronics prototyping platform based on flexible, easy-to-use hardware and software.
Founded by Massimo Banzi and David Cuartielles in 2005.
An open-source hardware platform based on Atmel AVR microcontroller and a C++ based IDE.
In-Expensive, Simple and easy to learn programing.
Controller independent programming language.
One language compatibility with all boards.
Single software for programming, compiling and burning the code.

## Slide 6: http://www.arduino.cc/
Arduino is an open-source electronics prototyping platform based on flexible, easy-to-use hardware and software. It’s intended for artists, designers, hobbyists, and anyone interested in creating interactive objects or environments.
  Processor: 16 Mhz ATmega328
  Flash memory: 32 KB
  Ram: 2kb
  Operating Voltage: 5V
  Input Voltage: 7-12 V
  Number of analog inputs: 6
  Number of digital I/O: 14 (6 of them PWM)

## Slide 8: Getting Started
Check out: http://arduino.cc/en/Guide/HomePage
  Download & install the Arduino environment (IDE)
  Connect the board to your computer via the USB cable. If needed, install the drivers
  Launch the Arduino IDE
  Select your board
  Select your serial port
  Open the blink example
  Upload the program

## Slide 9: Arduino IDE
Button Bar
Menu Bar
Actual Code
Program Notification Area
Status Bar

## Slide 11: Parts of the Sketch

## Slide 12: Select Board

## Slide 13: Select com port

## Slide 14: First program
int ledPin = 13; void setup()
{
pinMode(ledPin, OUTPUT);
}
void loop()
{
digitalWrite(ledPin, HIGH); delay(2000); digitalWrite(ledPin, LOW); delay(2000);
}

## Slide 15: Bread Board

## Slide 16
Happy Coding
Journey begins from here……